## Slide 1: Transmitter Localization and Optimizing Initial State in Classical/Quantum Sensor Networks
Thesis Defense – Jan. 23, 2024
Caitao Zhan
Committee: Himanshu Gupta, Samir Das, C.R. Ramakrishnan, Nengkun Yu, Mark Hillery

## Slide 2: Table of Contents
Content | Paper | Time
Part 0: Introduction & Motivation |  | 8 min
Part 1: Transmitter Localization in classical sensor networks | ACM/IEEE IPSN 2020 IEEE WoWMoM 2021 Elsevier PMC 2022 | 16 min
Part 2: Transmitter Localization in quantum sensor networks | IEEE QCE 2023 | 14 min
Part 3: Optimizing Initial State in quantum sensor networks | ACM TQC (under revision) | 14 min
Summary |  | 

## Slide 3: RF spectrum
Electromagnetic spectrum with frequencies from 3 Hz to 3000 GHz
  Sweet spot: hundreds of MHz to a few GHz
Limited natural resource in great demand due to increasing number of wireless devices

## Slide 4: Shared Spectrum
Authorized user: users with license, incumbents (highest priority)
Unauthorized user: users without license. Use spectrum opportunistically
  Should not affect authorized users

## Slide 5: Problem -- Interference
Problem: Unauthorized users (intruders) transmitting illegally will interfere against the authorized users
Bad Solution: Detect spectrum violations via complaints and manual investigation
  Human intensive and time-consuming
Motivated by the above, we seek an effective way to accurately localize multiple intruders simultaneously – Multiple transmitter localization (MTL)

## Slide 6: Wireless Sensor Networks (WSN)
Intruders
MTL via Classical Sensor Networks

## Slide 7: Classical vs. Quantum Sensor
Classical sensor
Wireless sensor: RSS, CSI
Image sensor: visible light
Acoustic sensor: sound wave
Quantum sensor
Single photon detector: single photon
RF-photonic sensor: optical quadrature displacement
Interferometry: light phase change
Rydberg atoms: electric field
Sensitivity:
above standard quantum limit
Sensitivity:
below standard quantum limit
Notes: The SQL arises from the Heisenberg uncertainty principle, [which states that there is a fundamental limit to the precision with which pairs of properties, such as position and momentum, can be simultaneously known]
SQL refers to the minimum level of quantum noise without using entanglement and squeezed states.

## Slide 8: Why Quantum Sensor?
Advances in quantum technologies efficient and sensitive quantum sensors for radio-frequency (RF) sensing
  Rydberg atom-based spectrum analyzer [1]: 0 to 20 GHz
  Quantum wireless sensing [2]: micro energy level of atoms vibration of water
  RF-photonic quantum sensors [3]: optics property amplitude/phase of radio signal
[1] Waveguide-coupled Rydberg Spectrum Analyzer from 0 to 20 GHZ, D. Meyer et al, PR Applied 2023
[2] Quantum Wireless Sensing: Principle, Design, and Implementation, F. Zhang et al, MobiCom 2023
[3] Demonstration of a reconfigurable entangled radiofrequency photonic sensor network, Z. Zhang et al, RPL 2020
Notes: much more sensitive than the classical antenna-based RF sensors.

## Slide 9: Table of Contents
Content | Paper | Time
Part 0: Introduction & Motivation |  | 8 min
Part 1: Transmitter Localization in classical sensor networks | ACM/IEEE IPSN 2020 IEEE WoWMoM 2021 Elsevier PMC 2022 | 16 min
Part 2: Transmitter Localization in quantum sensor networks | IEEE QCE 2023 | 14 min
Part 3: Optimizing Initial State in quantum sensor networks | ACM TQC (under revision) | 14 min
Summary |  | 

## Slide 10
Authorized user
Intruder
Sensor
Location?
Location?
Sensor
Part 1.1 -- Efficient Localization of Multiple Intruders in Shared Spectrum Systems (IPSN 2020)
Authorized user
Intruder
Notes: Consider a geographic area, some authorized users
Crowdsourced a lot of sensors. Sensors report RSS
Three types of transmitters: Primary, secondary, intruders.

## Slide 11: Problem Definition
MTL-SS: given the observations from the sensors, locate the intruders
Challenges:
Sensor receives only an aggregated sum of the signals from the multiple intruders transmitting simultaneously. Signal assume not-separatable
Multiple targets to localize, some might be close to each other.
Dynamically changing authorized users in the background.
MTL: not considering background authorized users
  Background authorized user issue can be solved using online training technique

## Slide 12: High-level Approach: Maximum a Posterior (MAP)
A hypothesis is a configuration of intruders, a set of (location, power) pairs.
Training data: Probability distributions (PDs) of RSS at sensor locations for each hypothesis
MAP: Given actual sensor observations of RSS, compute the following Bayes formula and pick the most likely hypothesis
A single hypothesis
actual observation
PD from training data

## Slide 13: Pros & Cons of MAP
Pros
  Optimal classification accuracy
  No need to assume a propagation model
  Allows to estimate intruders’ power
  Extends to solve MTL-SS problem with background users
Cons:
  High computation cost
    Divide-and-conquer
  High training cost
    Novel Interpolation
    Only train for a single intruder, assuming conditional independence, and utilizing (linear) power summations for constructing multiple intruder data

## Slide 14: MAP*: Optimizing MAP
Core idea: Divide-and-conquer
Far-away isolated intruders can be localized independently Procedure 1
Close-by intruders in a cluster are localized Procedure 2
Procedure 1: isolated intruders
Hypothesis represents a single intruder
Run MAP at appropriate local areas
Procedure 2: Multiple intruders close-by
Hypothesis represents two or three intruders
Construct multi-intruder PDs from training data of single intruders
Run MAP at appropriate areas
Notes: value of (power of the sum) of multiple signals equals to (sum of the powers) of those individual signals. linear power here.

## Slide 15: MAP* Illustration
Intruder
Sensor
Sensor
Procedure 1
Procedure 2
Procedure 1
Notes: Let’s illustrate the problem
Any questions for this?
We can observe that MTL is easier than MTL-SS.
We will solve MTL first, and then MTL-SS.

## Slide 16: Evaluation – MAP*, Simulation
MAP* (red bar) has lower localization error
and lower sum of miss rate and false alarm rate.
Compared with 1) Clustering-based solution, 2) SPLOT (MobiCom 2017)
Evaluation metric: localization error, miss and false alarm rate
Notes: Localization performance of various algorithms in a large scale simulation, for varying number of intruders

## Slide 17: MAP*, Indoor Testbed
SDR devices and
single board computers
MAP* has lower localization error
and lower sum of miss rate and false alarm rate.
Notes: Localization performance of varies algorithms in an indoor testbed, for varying number of intruders

## Slide 18
MAP*, Outdoor Testbed
MAP* has lower localization error
and lower sum of miss rate and false alarm rate

## Slide 19: Part 1.2 -- DeepMTL: Deep Learning Based Multiple Transmitter Localization (WoWMoM 21, PMC 22)
Same background and problem
Use deep learning for performance improvement
Notes: The sensors will sense the wireless channel of interest and process the wireless signals. Then sensors compute the received signal strength.

## Slide 20: Core Idea: a Two Step CNN-based Method
Input
sensor1: (x1, y1, RSS1)
sensor2: (x2, y2, RSS2)
sensor3: (x3, y3, RSS3)
…
Output
Tx1: (x1, y1)
Tx2: (x2, y2)
Represent the sensor input as an image
Apply image-to-image translation CNN model
Apply object detection CNN model
Step 1
Step 2

## Slide 21: Step 1: Image to Image Translation
Input / Output Representation
Gaussian
Peak
translation
Notes: Map one sensor to a pixel in the input representaiton

## Slide 22: Step 1: Image to Image Translation
sen2peak: the CNN model
Loss function
4 layers
Notes: C[input-channel, output-channel, kernel-size, stride, padding]
G[number-of-groups, number-of-channels]

## Slide 23: Step 2: Peak Detection
YOLO (You Only Look Once): A popular object detection model.
  Localizing objects in an image
TX’s distribution is a peak. We view a peak as an object.
  Peak detection is object detection
We customize the YOLOv3 (106 layers) and introduces YOLOv3-cust
The output of YOLOv3-cust are the coordinates of the center of the red bounding boxes
Notes: A simple way: use a local maxima-based method (maximum pixel value within a circle of a certain radius)
Problem: Setting the radius value and the threshold for peaks is ad-hoc
Need a more intelligent method.

## Slide 24: Evaluation -- Setup
Data generated using a simulator called SPLAT!
~100K samples for training and ~20K samples for testing
  Area = 1km x 1km, grid = 100 x 100, cell = 10m x 10m
Performance metrics:
  Localization error
  Miss rate / False alarm rate

## Slide 25: Compare Localization Error of Three Different Step 2 Methods (sharing the same step 1)
  DeepMTL: use customized YOLOv3
  DeepMTL-yolo: use the original YOLOv3
  DeepMTL-peak: use naive peak detection

## Slide 26: Compare Localization Error (Varying # of TX)
Compare our proposed DeepMTL with MAP*, SPLOT and DeepTxFinder

## Slide 27: Compare Miss & False Alarm rate (Varying # of TX)
Compare our proposed DeepMTL with MAP*, SPLOT and DeepTxFinder

## Slide 28: Part 1 Conclusion
Developed an efficient method based on Bayesian and Divide & conquer for the multiple intruder localization (MTL) problem
Designed and implemented a novel 2-step deep learning based approach named DeepMTL for the multiple transmitter localization problem
The evaluation results show that our methods outperforms the prior work by a large margin.

## Slide 29: Table of Contents
Content | Paper | Time
Part 0: Introduction & Motivation |  | 8 min
Part 1: Transmitter Localization in classical sensor networks | ACM/IEEE IPSN 2020 IEEE WoWMoM 2021 Elsevier PMC 2022 | 16 min
Part 2: Transmitter Localization in quantum sensor networks | IEEE QCE 2023 | 14 min
Part 3: Optimizing Initial State in quantum sensor networks | ACM TQC (under revision) | 14 min
Summary |  | 

## Slide 30: Part 2: Quantum Sensor Network Algorithms for Transmitter Localization (IEEE QCE 2023)
Transmitter
Quantum Sensor
Given from the quantum sensor network, localize a single TX
Location?
Quantum Sensor
Qubits: a complex
value vector of size

## Slide 31: Intro: Quantum Measurement
A quantum mechanics postulate, defined by some operators
If the measurement is carried on a pure state , we see the outcome with probability
General quantum measurement is described by positive operator-valued measure (POVM)

## Slide 32: Intro: Quantum State Discrimination (QSD)
Preparation
Discrimination
Preparation: Pick a quantum state from a target set
Discrimination: Determine what is by measuring it
Picked
Measured as
Picked
Measured as
measurement

## Slide 33: Problem Definition of TX Localization in QSN
A transmitter and distributed set of quantum sensors (QSN) in an area
QSN in an initial state of
QSN evolve into a final state under the impact of a transmitter over a period of , where models the quantum sensing
Estimate the location of the transmitter based on final state

## Slide 34: Related Work
“Distributed Quantum Sensing Network with Geographically Constrained Measurement Strategies”, Yingkang Cao & Xiaodi Wu, IEEE ICASSP 2023
  Local measurement
“Discrete Outcome Quantum Sensor Networks”, Mark Hillery & Himanshu Gupta & Caitao Zhan, Physical Review A, 2023
  Global measurement, estimate discrete parameters
  Precursor work of Part 2 and Part 3
  Part 2 attempts to explore QSN towards real life application (TX localization)
Notes: teleportation to central node

## Slide 35: Quantum Sensing Model
: operator that models the impact of a signal to a quantum sensor
  For impact on multiple sensors, do tensor product,
Assume Hamiltonian is a function of electric field is a function of distance () connection between and can be built
Notes: Intuition: The further the distance from the TX to the sensor, the weaker the impact from the TX to the sensor
The electric field amplitude () will decrease as the signal travels further in space
Intuition: The further the distance from the TX to the sensor, the weaker the impact from the TX to the sensor
Observation: The electric field amplitude (𝐸) will decrease as the signal travels further in space

## Slide 36: Quantum Sensing – Phase Shift
The key quantity: phase shift picked up by the quantum sensor due to interaction with the signal [1]
Time evolution operator due to a signal :
Phase shift, , accumulated during sensing time due to the signal [1]:
[1] Quantum Sensing, C. Degen & F. Reinhard & P. Cappellaro, Review of Modern Physics 2017
Notes: is the coupling of the qubit to the signal
𝛾 is the coupling of the qubit to the signal

## Slide 37: Methodology: TX Localization as QSD
Pose the TX localization problem as the quantum state discrimination (QSD)
Observation: Different locations of TX will result in different final states
Key idea: by determining the final state (via QSD), we get the TX location
[1] Quantum State Discrimination and Its Applications, J. Bae, J. Phys. A: Math. Theor., 2015
Notes: Underlies various applications in quantum information processing
Describes the distinguishability of quantum systems in different states, and the process extracting information from quantum system.

## Slide 38: One-Level QSD Method
The quantum sensor network is in initial state
Create the set of final states corresponding to the center of grid cells.
Generate the POVM on the final states using Pretty Good Measurement [1]
Localize the TX by a QSD over the final state using POVM . Multi-shot, select most frequent outcome
[1] A ’Pretty Good’ Measurement for Distinguishing Quantum States, Paul Hausladen et al, Journal of Modern Optics 1994

## Slide 39: Improve: Parameterized Quantum Circuits
QSD-based method is good in theory, but…
  POVM is hard to implement on gate-based quantum machines
  QSD-based method is limited to discrete TX locations
Solution:
  POVM parameterized quantum circuits
  Learn the parameters via training (a.k.a. quantum machine learning)
  Add a fully connected layer that can output in either discrete or continuous space (via different labels and loss function)
Notes: High PoE: assign a single outcome to a set of target locations

## Slide 40: PQC-based Localization
Quantum part: blocks of and
Classical part:
  Process the measurement outcomes, i.e.,
  Neural network location predictor
    Classifier
    Regression
Notes: measurement: compute the expected value of the z operator (measurement)
overall circuit with the Classifier component for the location prediction essentially equates to a circuit for quantum state discrimination (QSD), as the QSD problem also outputs a finite number of discrete outcomes
To output the predicted location in the continuous 2D space, we use a Regression Variant that outputs the location as an (x, y) point.

## Slide 41: Evaluation Setting
Area grid
  Cell size:
  Grid size: to
TX signal’s electric field model:
  [1]
  : power of the TX
  : is the distance between TX and sensor
  : wireless propagation noise, zero mean gaussian
Sensor setting:
  Initial state: Uniform superposition state
  Number: 4, 8, 16
  Uniformly distributed
TX Location:
  Continuous : anywhere in the grid – Average localization error
  Discrete : only at cell centers – Cell classification accuracy
[1] Field strength meter, https://en.wikipedia.org/wiki/Field_strength_meter
Notes: Evolution time = 1 ms
Less than one micro watt

## Slide 42: Evaluation Result
The PQC-based is better than QSD-based method
Two level approach can improve the localization performance

## Slide 43: Conclusion & Discussion
A first step using QSN in a real-world application – localization of TX
  Pose the TX localization problem as quantum state discrimination
TX Localization using QSN: meter level localization accuracy ()
  Not better than using classical wireless sensors (yet)
  But the TX power is very small classical sensor may not even detect it
Potential future directions:
  Entangled initial state
  A better/realistic Hamiltonian
  New localization algorithms

## Slide 44: Table of Contents
Content | Paper | Time
Part 0: Introduction & Motivation |  | 8 min
Part 1: Transmitter Localization in classical sensor networks | ACM/IEEE IPSN 2020 IEEE WoWMoM 2021 Elsevier PMC 2022 | 16 min
Part 2: Transmitter Localization in quantum sensor networks | IEEE QCE 2023 | 14 min
Part 3: Optimizing Initial State in quantum sensor networks | ACM TQC (under revision) | 14 min
Summary |  | 

## Slide 45: Part 3: Optimizing Initial State of Detector Sensors in Quantum Sensor Networks (ACM TQC, revision)
A network of quantum sensors. Sensor’s output is binary (detect / no detect)
The sensor network is initialized in
One sensor detects an input, i.e., impacted by a unitary U
The sensor network evolves into a final state
Task: Measure the final state to figure out which sensor detected
Problem: The optimal initial state for the quantum sensor network?
  Need to consider the quantum measurement too
Initial State?
Measurement?
Sensor # detected
Notes: Binary: (detects an input / does not detect an input)

## Slide 46: – Interaction between Input and Sensor
the rotation of a spin caused by a magnetic field
a phase shift induced in a state of light by a transparent object
Assume is eigen-decomposed as
…

## Slide 47: Final States
Sensors
Initial State
N Final States
Final States

## Slide 48: Apply QSD to our Problem
We model a quantum sensor network using techniques from quantum state discrimination (QSD)
Figuring out which sensor detects Quantum state discrimination (QSD) against the N final states
The QSD outcome tells which sensor detected an input
Quantum State Discrimination
POVM
Detected Sensor
N Final States
Quantum Sensor Network

## Slide 49: Semidefinite Programming
Given N final states , designing an optimal POVM such that discriminating the N final states has a minimal error:
Numerically solvable via semi-definite programming (SDP) [1]
The solver (CVXPY) will give you
  POVM, i.e., measurement operators
  objective value – minimal probability of error
[1] Designing optimal quantum detectors via semidefinite programming, Y.C. Eldar, IEEE Trans. Information Theory, 2002
Initial State?
Objective value
Heuristic algorithm to search for the optimal initial state!
SDP

## Slide 50: Heuristic Search Algorithms
Initial state search space: A complex value array
  where is the number of sensors (one qubit per sensor)
Random
Find some neighbors of
Compute the objective value of the neighbors
The best neighbor is . Let
Go back to step 2) until termination condition satisfied
Return
Hill Climbing:
We also tried simulated annealing and genetic algorithm
Climbing

## Slide 51: Results for Heuristic Search
Note:
Exist a such that in , zero error in figuring out which sensor detects
  exist an initial state such that the final states are mutually orthogonal

## Slide 52: Expression for
n | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
T (degree) | 60 | 60 | 65.9 | 65.9 | 69.3 | 69.3 | 71.6 | 71.6
The larger the number of sensors, the larger the
Notes: What does larger T imply?
A larger T – a larger angle means U has a larger impact to the sensor
Larger number of n means it is harder for discrimination

## Slide 53: 2 Key Steps in Proof
Construct new basis that are tensor products of and
Partition the amplitude squares
  }
  ,
  }

## Slide 54: Case – Analysis
Express in the basis of , , |}, and the respective amplitudes are
Inner product
The possible values of are illustrated inside the red triangle below

## Slide 55: Case: Optimal
Optimal
Optimal
maximize minimize
and
minimize |

## Slide 56: General Sensors, Optimal Initial State
, independent
Optimality near proved
Optimality proved
Dicke State!
Where is and is
“Modification of Dicke State”
dependent
Where is and is
E.g., when
E.g., when
Notes: Dicke state
>T proof: letting the pairwise inner products equal zero
<T proof: symmetry of coefficient
Dicke state |𝐷_𝑘^𝑛 ⟩=1/(𝑛¦𝑘)^2 ∑2_(𝑥∈{0,1}^𝑛, 𝑤𝑡(𝑥)=𝑘 )▒〖|𝑥⟩〗
>T proof: letting the pairwise inner products equal zero
<T proof: symmetry of coefficient

## Slide 57: Acknowledgement
Committee:
Coauthors:
Many more!

## Slide 58: Summary – 3 Topics
  Multiple transmitter localization in classical sensor networks
  Transmitter localization in quantum sensor networks
  Initial state optimization for detector sensors in quantum sensor networks
  Thank you for listening!